## Slide 1
Proximity Detection with Single-Antenna IoT Devices
Timothy J. Pierson, Travis Peters, Ronald Peterson, and David Kotz
Department of Computer Science, Dartmouth College, Hanover, NH, USA 03755
Internet of Things (IoT) devices may frequently encounter new devices
51%
CAGR
CAGR = Compound Annual Growth Rate
[1] Berg Insight. Wireless IoT connectivity technologies and markets. Online at http://www.berginsight.com/ReportPDF/Summary/bi-globalm2m7-sum.pdf
[2] Institute of Electrical and Electronics Engineers. 802.11n standard. Online at http://standards.ieee.org
[3] Constantine A. Balanis. Antenna Theory: Analysis and Design. Wiley, third edition, 2005
Proximity can be a basis for trust when devices are first encountered
Use repeating portions of Wi-Fi Long Training Field (LTF) for proximity
Near-field effects can cause mismatches in the repeating LTF
Repeating portions mismatch at close range, but not at long range
National Science Foundation
Award CNS-1329686
T1 and T2 are identical 64-sample portions of the Long Training Field in the Wi-Fi preamble2
Repeated LTF portions T1 and T2 are used for channel estimation
T1 and T2 are expected to match at the receiver (plus noise)
All Wi-Fi receivers must evaluate T1 and T2
Even single-antenna devices can measure T1 and T2
In the reactive and radiating near-field regions around a transmitter, the electric and magnetic fields are not yet aligned
Fields form a vector that rapidly rotates in time in a plane parallel to the direction of propagation3
Rotation causes mismatches between T1 and T2
With Wi-Fi, near-field effects extend to roughly 14 cm from transmitter
Analysts predict billions of IoT devices will be deployed in the near future1
IoT devices are envisioned to share data among themselves
Some shared data may be privacy sensitive or have security implications
With billions of devices deployed, a device may encounter dozens of new devices every day
T1 and T2 on all Wi-Fi subcarriers
T1 at 6 cm
Expected location
T2 at 6 cm
T1 at 30 cm
T2 at 30 cm
6 cm
30 cm
Proximity is detected if the mismatch is over a fixed threshold
At is the sum of the Euclidean distance between T1 and T2 over all 64 subcarriers
At is high at close range, low at long range
Declare proximity if At is above a fixed threshold
lt = length of transmitting antenna
λ = wavelength
D = length of transmitting antenna + length of receiving antenna
R1 = estimated range of reactive near-field region
R2 = estimated range of radiating near-field region
Wi-Fi Preamble
Assume an adversary is not able to gain close physical proximity to devices (e.g., adversary does not break into a home to gain physical proximity)
Proximity can then serve as a basis for trust
Techniques exist for multi-antenna devices to detect proximity
No proximity techniques exist for single-antenna devices
Distant adversary
Nearby legitimate devices
Average At of 1,000 frames transmitted from each antenna type shown